## Slide 1: Handshakes and modes in 2011

## Slide 2: Handshakes
Communication protocol over DIP between LHC & experiments
Goal: inform EXP’s about any critical action to be performed by the machine and get detectors confirmation they are in SAFE STATE before starting the action
5 different handshakes:
  LHC_INJECTION
  LHC_ADJUST (↔ STABLE BEAMS)
  LHC_BEAMDUMP (↔ STABLE BEAMS)
  LHC_TI2_SETUP
  LHC_TI8_SETUP
EDMS doc 1031913
DATABASE RESTRICTION: two handshakes (or more) cannot be started at the same time. Only LHC_TI2/TI8_SETUP can start at the same time
↔ TRANSFERLINE SETUP (ALICE/LHCb ONLY )

## Slide 4
Beam dump handshake becomes informative

## Slide 5: LHC Modes
Summary status of the operational activity. Distributed for:
  information
  conditioning sub-system response (e.g. experiments operation, movable devices allowed in beam)
There are two modes:
  ACCELERATOR MODE: provides a general overview of the machine activity (e.g. proton physics, access, shutdown, etc.)
  BEAM MODE: provides the state of the machine with regard to the machine cycle (e.g. injection, ramp, etc.)
EDMS doc 865811

## Slide 6
TABLE IMPLEMENTED IN THE DATABASE AS CONSTRAINT; ONLY THIS COMBINATION OF ACCELERATOR VS BEAM MODES ALLOWED

## Slide 7: Automatic and systematic end of fill
Experiments request a systematic way of signaling the end of fill=end of data taking in order to trigger the end of fill statistics  this will be done with the mode BEAM DUMP
PROGRAMMED DUMP  handshake and programmed dump sequence
UNPROGRAMMED DUMP  logic (SIS): once BEAM MODE = STABLE BEAMS if B1/B2 BIC LOOP OPEN  beam mode will be automatically changed to BEAM DUMP

## Slide 8: INJECTION PHYSICS BEAM
SIS will monitor the intensity value and once the safe beam limit is passed will trigger the automatic change of the beam mode to INJECTION PHYSICS BEAM