## Slide 1
Aperture measurements
R. Bruce
R.W. Assmann, M. Giovannozzi, G. Mueller, S. Redaelli, D. Wollmann
Acknowledgement:
C. Alabau Pons, R. de Maria, S. Fartoukh, J. Wenninger, G. Vanbavinckhove

## Slide 2: Outline
Global aperture measurements
  Method
  Results
Local measurements of IR triplet aperture
  Method
  Results
Conclusions
Future work

## Slide 3: Global measurements – emittance blowup technique with collimator scan
Start with all collimators are retracted, provoke beam losses by crossing the 3rd order resonance (measurements done per beam and plane)
Signals on BLMs recorded to identify aperture bottleneck
Primary collimators (TCPs) closed in steps, losses provoked on each step
When main loss peak moves to the TCP the aperture is shadowed
The known gap of the TCP used as aperture estimate
For method see R. Assmann, presentation in Commissioning working group
BEAM
BEAM
TCP
TCP
Aperture
Aperture

## Slide 4: Global measurements – method
Example: B2 ver BLM signals as function of TCP opening
Aperture calculated with 3 methods
  No normalization
  Normalized to intensity loss
  Normalized to intensity loss and max signal with no shadow
TCP
Q4R6
TCP
Q4R6
TCP
Q4R6
Method 3, Aperture=12.8σ
Method 2, Aperture=13.1σ
Method 1, Aperture=13.1σ

## Slide 5: Global measurements - results
log book, 1s BLM integration |  | 
 | H | V
B1 | 12 | 13
B2 | 12.5 | 13.1
5s BLM integration time |  | 
Method 1: no normalization |  | 
 | H | V
B1 | 11.4 | 13
B2 | 13 | 13.1
Method 2: normalizing by intensity loss |  | 
 | H | V
B1 | 11.7 | 
B2 | 13 | 13.1
Method 3: normalizing by intensity loss and response |  | 
 | H | V
B1 |  | 
B2 | 12.9 | 12.8
 | H | V
B1 | Q6R2 | Q4L6
B2 | Q5R6 | Q4R6
Aperture found (σ)
Location of bottlenecks found
Locations consistent with 2010
2010 |  | 
 | H | V
B1 | 12.5 | 13.5
B2 | 14 | 13

## Slide 6: Local measurements - method
All collimators retracted
Global aperture known from previous measurement
Orbit bump with known amplitude introduced in steps triplet
Losses at global bottleneck and triplet monitored with BLMs
Loss peak moves to triplet when it shadows global aperture
Triplet aperture = global aperture + orbit excursion
BEAM
Global bottleneck
Triplet
BEAM
Global bottleneck
Triplet
BEAM

## Slide 7: Local measurements - method
One measurement per beam per IP per plane
  Only crossing plane considered
Example: IR1 B1 V
Q4L6
Q2R1
Q2R1
Q2R1
Method 3, Aperture=16σ
Method 2, Aperture=16.5σ
Method 1, Aperture=16.5σ
Q4L6
Q4L6

## Slide 8: Local measurements - results
IR1 triplet V |  |  | IR5 triplet H |  |  | IR2 triplet V |  |  | IR8 triplet H |  |  | 
log book, 1s BLM integration |  |  | log book, 1s BLM integration |  |  | log book, 1s BLM integration |  |  | log book, 1s BLM integration |  |  | 
B1 | 16 |  | B1 | 15.5 |  | B1 | 14.5 |  | B1 | 16 |  | 
B2 | 15 |  | B2 | 17 |  | B2 | 15 |  | B2 | 16 |  | 
5s BLM integration time |  |  | 5s BLM integration time |  |  | 5s BLM integration time |  |  | 5s BLM integration time |  |  | 
Method 1 |  |  | Method 1 |  |  | Method 1 |  |  | Method 1 |  |  | 
B1 | 16.5 |  | B1 | 15.2 |  | B1 | 14.6 |  | B1 | 15.5 |  | 
B2 | 15.3 |  | B2 | 17.7 |  | B2 | 16.4 |  | B2 | 15.5 | (at TCTVB.4R8, not in triplet) | 
Method 2 |  |  | Method 2 |  |  | Method 2 |  |  | Method 2 |  |  | 
B1 | 16.5 |  | B1 | 15.2 |  | B1 | 14.7 |  | B1 | 15.5 |  | 
B2 | 15 |  | B2 | 17.8 |  | B2 | 16.8 |  | B2 | 15.7 |  | 
Method 3 |  |  | Method 3 |  |  | Method 3 |  |  | Method 3 |  |  | 
B1 | 16 |  | B1 | 15.1 |  | B1 | 14.6 |  | B1 | 15.6 |  | 
B2 | 16.2 |  | B2 | 17.3 |  | B2 | 16.4 |  | B2 | 15.6 |  | 
Method 2: normalizing by intensity loss
Method 3: normalizing by intensity loss and response
Method 1: no normalization

## Slide 9: Summary of triplet aperture measurements
Aperture in crossing plane (σ) | B1 | B2
IR1 V | 16 | 15-16
IR5 H | 15 | 17
IR2 V | 14.5 | 15-16.5
IR8 H | 15.5 | 15.5
  IR1 and IR5 relevant
  Measured triplet aperture in IR1/5 up to 1 σ larger than assumed in Evian
  Detailed analysis taking into account orbit, beta-beat etc still to be done
  Triplet aperture from n1 using nominal tolerances: ~8.9 σ (M. Giovannozzi)
  Discussion with concerned parties on tolerances in n1 model needed
assumed | 2010 | 
 | H | V
B1 | 14.5 | 15.5
B2 | 16 | 15

## Slide 10: Conclusion
Global aperture measurements show the same bottlenecks as last year’s measurement
  Found global aperture: 11.5-13 σ
  Global aperture seems worse than 2010 by up to 1.5 σ
Some open questions (strange data points etc) – need to look into logging data
Local scans in triplets performed
  Triplet aperture measured to above 15 σ
  Equal or up to 1 σ larger than assumed 2010
  Detailed analysis of implications for β* still to be done
All apertures expressed in terms of σ at primary collimator
  Beta-beat @ TCP < 6% (input from G. Vanbavinckhove)
Around 1 σ uncertainty

## Slide 11: Future work
Local triplet aperture measurements with dilluted pilot beam at squeeze and top energy
  Define a beam edge using the primary collimator, then increase bump amplitude in triplet until a loss is observed. Same method as in 2009.
Aperture measurement in the dispersion suppressor downstream of IR7
  Gives response of BLM at location of highest cleaning inefficiency
Comparison with the method used in 2009 also at injection