## Slide 1
Frequency characteristics of
damper versus growth rates
450 GeV – part 1
W. Hofle
Acknowledgements:
N. Mounet, E. Metral, D. Valuch

## Slide 2
N. Mounet
Rise-times computed for full machine @50 ns bunch spacing
10 MHz

## Slide 3
Damper gain versus frequency (1)
power amplifier / kicker simplified model, PAC 2001
Capacitances and resistor determine 3 dB point
detailed simulations see LHC Project-Note-259, 2001

## Slide 4
1-pole roll-off at 1 MHz, with phase compensated by a digital filter
30% less gain at 1 MHz than at 3 kHz …
some tuning of phase compensation needed when we go to 25 ns spacing, i.e.  20 MHz
quality of compensation of cable losses by analog filter recently checked (D. Valuch)
further checks can be done in next technical stop, no surprises expected
Damper gain versus frequency (2)
kick @ 10 MHz,
10% left
measured on power amplifier
(blue curve on kicker,
green on anode of tetrode)
LHC-PROJECT-REPORT-1148

## Slide 5
40 turns, 1/40 = 0.025

## Slide 6
sufficient damper gain available at 450 GeV to damp all coupled bunch dipole modes
growth-rate of instabilities has zero @10 MHz (half bunch repetition frequency)
should we put a notch here for the damper gain, too ?
computed growth rates do not support increase of “damper gain versus frequency”
concerning observation: individual bunches seem to be not stable sometimes:
 here a flat gain of the damper with frequency might help,
but the implementation is only possible at an expense of signal/noise ratio possible
should we pursue this in a test/MD ?
Conclusions (450 GeV)