## Slide 1: LHC Longitudinal Blow-up
LHC Longitudinal Blow-up
Reported by P. Baudrenghien CERN-BE-RF
Acknowledgments to:
T. Mastoridis
for the analysis of the many bunch profiles and for preparing the corresponding slides
M. Jaussi
for the quick modifications to the RF Controls involved in the blow-up
D. Jacquet
  for the RF functions needed for the blow-up

## Slide 2
Longitudinal blow up, why
Longitudinal blow up, how
Performances
Improvements

## Slide 3: Longitudinal blow-up. Why?

## Slide 4: Single-bunch longitudinal stability
Broadband stability criteria
The RHS is proportional to
Without blow-up the threshold quickly decreases during the acceleration ramp
With a blow-up that keeps bunch length constant (for example), the threshold increases linearly with the RF voltage
See: E. Shaposhnikova, Longitudinal Beam Parameters during acceleration in the LHC, LHC Project Note 242, Dec 2000

## Slide 5: Winter 2010. Ramping pilot without blow-up
March 26th 2010: Single bunch pilot in both rings, ~ 0.2 eVs. 8 MV at injection (fs0=65.3 Hz), increased to 12 MV before ramp (fs0=80 Hz), constant 12 MV during acceleration ramp (fs0= 28.9 Hz @ 3.5 TeV) . BQM was not calibrated.

## Slide 6: Ramping nominal bunch intensity without blow-up
Inject 1.1E11, 1.2-1.3 ns long, 0.3-0.4 eVs
Capture with 5 MV (matched voltage ~ 3 MV)
Raise voltage to 8 MV before start ramp. Ramp with constant 8 MV
Very unstable. The bunch shrinks down to < 0.5 ns and we lose Landau damping
May 15th2010. First attempt to ramp nominal intensity single bunch. Bunch length during ramp. The longitudinal emittance is too low (<0.4 eVs). The bunch becomes unstable

## Slide 7: Longitudinal blow-up. How?

## Slide 8: Longitudinal emittance blow up
Phase noise spectrum
Part of the bunch excited
Inspired from the method used in the SPS (see reference below)
We apply Phase noise in the cavity field
We use a Rectangular Phase Noise Power Spectral density that excites only the core
  hit: 6/7 fs < f < 1.1 fs
    corresponds to a 1.20 ns window in the core
  and follow fs along the ramp
    from Hz to Hz
Algorithm to adjust the amplitude of the excitation xn from a measurement of the instantaneous bunch length (mean) Ln and comparison to target L0
Target bunch length L0 originally set at 1.2 ns
J. Tuckmantel et al., Study of Controlled Longitudinal Emittance Blow-up for High Intensity LHC beams in the Cern SPS, EPAC 08, Genoa

## Slide 9: Functions
Excitation spectrum, algorithm gain and target length are functions in the ramp
Synchrotron freq plus lower and upper frequency limits of the flat noise PSD
Target bunch length during ramp
Algorithm gain g during ramp

## Slide 10: Why more tricky in 2011?
Bunch Length Mean and Noise Amplitude during Ramp
Situation 2011: Because the capture voltage is mismatched, the 1.5 ns long SPS bunch shrinks to ~1.20 ns after capture. With a 1.2 ns target value for bunch length, excitation must start immediately as soon as the ramp starts. We typically end-up a bit short of the demanded 1.2 ns and observe “jumps” in bunch length measurements when bunch profile changes (non-adiabatic)
Situation 2010: Thanks to the matched capture the bunch shape is not changed much at injection. It is ~1.5 ns at the start of the ramp. The first part of the ramp proceeds smoothly without blow-up, with adiabatic bunch length reduction till it reaches the demanded 1.2 ns.

## Slide 11: Performances

## Slide 12: Example: Fill 1856 (June 7th)
Before “jump”
After “jump”
Increasing excitation but bunch keeps shrinking
We finish ramp at 1.1 ns
We start ramp at 1.3 ns

## Slide 13: Movie. Fill 1856.
First bunch of 12b batch B1, from t=0 at start ramp to t=1000 with t=650 at end ramp
Start at 1.3 ns, ends at 1.1 ns

## Slide 14: Trimming various functions.
Original
Changing target along ramp
Frequency max trim
Frequency min trim
1.1 ns B1, 1.2 ns B2
1.21 ns B1, 1.2 ns B2
B1 only, 1.18 ns
1.2 ns B1, 1.14 ns B2

## Slide 15: FWHM vs. 4-sigma Gaussian Fit
Original
New blow-up function
Frequency max trim
Frequency min trim
Comparison of FWHM sqrt[2/ln 2] and Gaussian Fit 4-sigma length from profiles at 40 Gsps. Not clear whether a Gaussian Fit would help

## Slide 16: Last 4 ramps
June 12th ramp started at 13:15
June 13th ramp started at 9:55
June 13th ramp started at 12:50
June 14th ramp started 06:45. We end-up with 1.12 ns B1 and 1.18 ns B2
Looks OK
Not that great…
1.12 ns B1 1.18 ns B2

## Slide 17: Improvements

## Slide 18: Improvements
Increase the bunch length measurement rate (presently 5 s between samples). The gain of the excitation control can then be increased to give more precision
Make blow-up more “gentle” to keep close to adiabatic (no change in bunch profile). Side-effect: length will go down to ~ 1 ns before rising back to 1.25 ns. Trial ramp.
Gaussian fit or brute force computation of variance in place of FWHM. Not sure it brings a decisive improvements when the evolution is not adiabatic
Installation of a second BQM crate in SR4 for developments
Keep observing/studying bunch profiles, cavity phase noise spectra and LLRF signals during blow-up

## Slide 19: Thank you for your attention…