## Slide 1: Update on plans for the first p-Pb run
John Jowett
With input from: R. Alemany, S. Hancock, M. Lamont, D. Manglunki, S. Redaelli, M. Schaumann, R. Versteegen J. Wenninger
For more information see pA@LHC workshop 4-8 June 2012
https://indico.cern.ch/conferenceDisplay.py?confId=182223

## Slide 2: Main questions
Clarification of physics priorities from LPC
  Any p-p reference data at 1.38 TeV/beam etc ?
Commissioning schedule
  Now moved into January 2013
  MD and possible pilot physics fill
Optics
  see Reine’s presentation
Filling scheme 100 ns or, now most likely, 200 ns
  LHCb
p-Pb and Pb-p
  Beam switch in middle of run (~ 1 day)
  ALICE polarity reversals in each beam direction ARE wanted (~ 1 day more)

## Slide 3: MD and pilot physics
RF synchronisation test with protons
  To be scheduled in regular MD time
Once we have Pb beam from SPS, we can do MD again
  Minimal goal: ramp many bunches (probably only a few Pb with many p)
Pilot physics (in physics time? ~16 h soon after MD?)
  Similar to what we planned last year
  No squeeze, few bunches to minimise set-up time and machine protection/collimation requirements

## Slide 4: Reminders!
This is a new mode of operation of LHC, almost unprecedented at any hadron collider.
Based on one very successful 16 hour MD
  Injection of some Pb in presence of many p bunches, with unequal revolution frequencies, without losses and enhancement of emittance growth
  Ramp of a few bunches, re-lock of frequencies
  First successful RF re-phasing (slow, not yet final system)
  CERN-ATS-Note-2012-051 (when fulltext available …)
Still to demonstrate (2nd MD cancelled last year)
  Injection and ramp of many bunches in both beams
  Faster RF-rephasing after RF frequency lock
  Optics with low β* in 3 experiments
  Off-momentum collision configuration
  All this integrated into efficient operational cycle

## Slide 5: Chamonix target p-Pb performance in 2012
Main choice: | Units | 200 ns |  | 100 ns | 
Beam energy/( Z TeV) | Z TeV | 3.5 | 4 | 3.5 | 4
Colliding bunches |  | 356 | 356 | 550 | 550
b* | m | 0.7 | 0.6 | 0.7 | 0.6
Emittance protons | µm | 3.75 | 3.75 | 3.75 | 3.75
Emittance Pb | µm | 1.5 | 1.5 | 1.5 | 1.5
Pb/bunch | 108 | 1.2 | 1.2 | 0.8 | 0.8
p/bunch | 1010 | 1.15 | 1.15 | 1.15 | 1.15
Initial Luminosity L0 | 1028 cm-2 s-1 | 6.2 | 8.3 | 6.4 | 8.5
Operating days |  | 22 | 24 | 22 | 24
Difficulty (subjective) |  | 0.9 | 1 | 0.9 | 1
Integrated luminosity | nb-1 | 15.4 | 22.4 | 15.9 | 23.1
Nucleon-nucleon | pb-1 | 3.2 | 4.7 | 3.3 | 4.8
Integrated luminosity by scaling from 2011 (c.f. ~7 pb-1 NN in Pb-Pb) Average Pb bunch intensities from best 2011 experience. Proton bunch intensities conservative, another factor 10 ??? Proton emittance conservative, another factor 1.37 ?
Should reduce by 0.6/0.8 m for recent change of b*
Untested moving encounter effects, possible reduction factor 0.1 ??

## Slide 6: Filling Scheme
Basic choice between 100 ns and 200 ns
  Construct same pattern for p and Pb
  Similar luminosity expectations
  200 ns better for separation around ALICE at this energy
Priority for ALICE
  Now that we are doing RF re-phasing, it should finally be possible to make bunch 1 collide with bunch 1 at IP2
  Maintain machine protection constraints on numbering
  Beam instrumentation and logging system (FBCT, BSRT, …) – will it all be transparent ?
Non-colliding bunches
  Presumed needed by ALICE, ATLAS, CMS
LHCb
  Lower priority – but we must take some collisions away from the others. How much? Displace one out of 15 batches?

## Slide 7: p-Pb 200ns scheme in 2012
LEIR
PS batch expansion bunch spacing = 200ns
SPS at extraction, after 12 transfers from PS,
Batch spacing = 225 ns minimum
(9 108 Pb ions / 3.6 s)
1.4 108
Harmonic number / Frequency
2
24-21 -169
16–14-12-24
200 MHz
2
Nb of bunches
2
24
PSB
PS batch compression bunch spacing = 200ns
SPS at extraction, after 12 transfers from PS,
Batch spacing = 225 ns minimum
(3 1010 protons)
1.2 1010
Harmonic number / Frequency
2+1
20-21 -84
9-10
200 MHz
2
Nb of bunches
2
24
1.5 1010
note: minimum batch spacing of 225ns dictated by protons injection at 26GeV/c
D. Manglunki, Chamonix

## Slide 8: p-Pb 100ns scheme in 2012
PSB
PS batch compression +splitting ; bunch spacing = 100ns
SPS at extraction, after 12 transfers from PS,
Minimum batch spacing = 225 ns
(6 1010 protons )
1.2 1010
Harmonic number / Frequency
Nb of bunches
LEIR
SPS at extraction, after 12 transfers from PS,
Minimum batch spacing = 225 ns
(9 108 Pb ions / 3.6 s)
1.4 108
Harmonic number / Frequency
2
24-21 -169
16–14-12-24
200 MHz
2
Nb of bunches
4
48
4
48
PS batch compression +splitting ; bunch spacing = 100ns
2
20-21 -84
9-10
3 1010
4.5 108
Note: minimum batch spacing of 225ns dictated by protons injection at 26GeV/c
D. Manglunki, Chamonix

## Slide 9: Optics for p-Pb operation – see talk by R. Versteegen
Small β* in IR1, IR2 and IR5 ?
  Need more aperture in triplet quadrupoles
  Greater sensitivity to perturbations
  Stronger chromatic effects (e.g., change of betatron oscillation frequency across the energy spread in the beam)
  For p-Pb, centre of energy distribution of beams have opposite sign shifts: chromatic variation (β-beating) of central optics
Heavy ion runs generally push optics further by adding lower β* at ALICE to preceding p-p optics.
In 2011 the additional squeeze to β*=(1,1,1,3)m was only just possible because of a still unidentified aperture restriction on the left of IP2.
    M., Giovannozzi, et al, IR2 aperture measurements at 3.5 TeV, CERN-ATS-Note-2012-017 MD, 2012.
We now propose baseline β*=(0.8,0.8,0.8,3)m with p-Pb
Try to validate β*=(0.6,0.6,0.6,3)m during set-up phase.
  Possible request from LHCb for 1-2 m ?
Try to get closer to parallel squeeze in all IPs – Jorg W et al

## Slide 10: Collimation set-up
Locking frequencies before squeeze means going through squeeze off-momentum
  Adjust collimator set-up throughout squeeze (IR3, TCTHs, …)
  Do it again after beam switch
How much do we really need to do
  Secondary collimators not so important for Pb beam
  Pre-calculate shifts for others ?
  How many loss maps really needed to validate ?
Consider locking after squeeze ?
  Why does it sound so scary ?

## Slide 11
Orbit at collimators,
3.5 TeV vs. 4 TeV
Additional collimator set-up will be required in squeeze
Vertical plane
Horizontal plane, zoomed in
Horizontal plane
x = orbit with δ offset,
x0= orbit with zero offset
R. Versteegen

## Slide 12: More predictions for p-Pb (no detail)
Bound-free pair production rate will be reduced to a few % of the Pb-Pb rate
  Luminosity losses in dispersion suppressors around experiments reduced, only on one side at a time
  Less irradiation, R2E, etc.
Similar scaling for electromagnetic dissociation
  Same equivalent photon spectrum of proton
  Somewhat reduced Pb beam losses in IR3
  Contributions from Pb collimation same as in Pb-Pb
Luminosity lifetime better than Pb-Pb
  Dominated by IBS of Pb beam or, maybe, beam-beam

## Slide 13: Proton beam evolution in collision (preliminary)
Few % loss in several hours
M. Schaumann
Other noise sources not in simulation.
Low intensity (10% of nominal) proton bunches have very weak IBS so shrink slowly due to synchrotron radiation damping.
Intensity loss from luminosity (cross section with Pb ~2 barn) is also small.
Vertical also shows damping.

## Slide 14: Pb beam evolution in collision (preliminary)
M. Schaumann
High intensity (150% of nominal) Pb bunches have strong IBS growth (as in 2011) despite having twice the synchrotron radiation damping of protons.
Fractional intensity loss from luminosity (cross section on Pb ~2 barn) is more significant, but much less than in Pb-Pb. Losses also from IBS debunching.
Few % loss in only 2.5 hours
Vertical shows damping.

## Slide 15: Luminosity evolution (preliminary)
Luminosity made by the bunches shown on previous two slides.
Slower decay than in Pb-Pb or even p-p fills.
We can hope for long fills which will increase the ratio of average to peak luminosity!
Good, since set-up will be longer than usual.
N.B. this is the worse case for luminosity decay, the higher intensity Pb bunches from the 200 ns filling scheme.
Caveats:
Unequal beam sizes may give beam-beam problems (but tune-shifts are still small).
This is still the conservative proton bunch intensity.
Not all physics in this simulation.

## Slide 16: Luminosity evolution during the run
Initial proton bunch intensity (10% nominal) is comparable with Pb in terms of bunch charge
  Unequal emittances …
Step up to full filling scheme with fixed bunch intensity as usual
  Pace may be determined by experiments’ requests
If all goes well, we will then try to increase luminosity by increasing proton bunch intensity
  Experiments should preferably be prepared for wide range in luminosity – less or more!
  Peak luminosity limits ? Adapt filling scheme?

## Slide 17: Conclusions, (some of) the actions needed
Continue with studies for optics, squeeze, etc.
  Possible optics corrections
BI, Experiments, Logging:
  Check that the shift of 1-1 collision point will not cause problems
Define filling schemes according to LPC priorities
Items to be scheduled (not today)
  RF synchronisation MD with p-p
  Many bunch p-Pb ramp MD
  Pilot physics fill
  Detailed commissioning plan
LHCb will have much less luminosity than other experiments (factor 60?)

## Slide 18: BACKUP SLIDes