## Slide 1: INCONSISTENCIES IN THE MQY TRANSFER FUNCTION
P. Hagen, E. Todesco
CERN, Geneva Switzerland
CERN, 7th August 2012
LBOC

## Slide 2: INCONSISTENCY IN MQY TRASFER FUNCTION
In general a superconducting magnet trasfer function has a spread of 5-15 units
  Typically 10 units – due to construction tolerances
  12 units in the 400 MQ
  11-12 units in the MQM
  6 in the MQXB
For the MQY we have in FiDeL 50 units
  Found by S. Fartoukh, study carried out by Per
Non consistent with previous works
  Memo giving 12 units [P. Hagen, E. Todesco, EDMS no. 879594, (2007)]
  ASC paper giving 8-9 units [N. Catalan Lasheras, B. Auchmann, G. Kirby, K.-H. Mess, R. Ostojic, and S. Russenschuck, IEEE Trans Appl Supercond 18 (2008)]

## Slide 3: INCONSISTENCY IN MQY TRASFER FUNCTION
Large spread due to a non negligible fraction of outliers
  Having 0.5-1% more transfer function

## Slide 4: INCONSISTENCY IN MQY TRASFER FUNCTION
MQY had two features
  Part measured at SM18, part only at room temperture
  Part of the magnets affected by high permeability collars (visible effect at room temperature, disappears at 4.2 K)
Inconsistencies present both in some cases with WM only, and in cases with 4.2 K test
The WM (uncorrected) had a spread of 23 units, 13 after correction

## Slide 5: ACTIONS
Revised table of transfer functions built, and differences w.r.t. present FiDeL data were worked out by Per
Rogelio found consistency in many cases with the beam based corrections of beta beating

## Slide 6: CONCLUSIONS AND ACTIONS
Clear sign of inconsistency of MQY TF model
  Relevant (1% errors on TF of some MQY – i.e. error different from beam1 to beam2 – becomes very relevant at squeeze)
  Presently partially corrected by beam based beta beating corrections
Correction of FiDeL needed
  Now or in LS1?