## Slide 1: UPDATE ON DECAY CORRECTION
N. Aquilina, E. Todesco
CERN, Geneva Switzerland
CERN, 3th May 2011

## Slide 2: WHERE ARE WE TODAY - REPRODUCIBILITY
Reproducibility of chroma decay at injection in 2011
  ±10 units in horizontal, ±5 units in vertical (two sigma)
  Not bad but it can be further improved
Measured decay of bare chromaticity at injection in 2011 [N. Aquilina]

## Slide 3: WHER ARE WE TODAY - REPRODUCIBILITY
The machinery for decay correction of tune and chroma is deployed and works [thanks Marek!  ]
  The implemented equations as proposed by L. Bottura, N. Sammut et al. are still valid, but ...
  the coefficients worked out through the magnetic measurements are obsolete due to change in cycling conditions
    Not last the reduced energy of the LHC ...
    But especially the ramp rate!
  Today we use an estimate of the coefficients based on a mix of beam measurements and magnetic measurements – it works and is much better than not doing any correction, but ...
  there is space for further improvement

## Slide 4: Different types of precYcle
Cycling strategy
  Measurements:
    Precycle of series measurements (50 A/s ramp of precycle, 12 kA flattop)
    Special measurements carried out in 2007-2010 (10 A/s ramp, 2 – 6 kA flattop) to better understand actual conditions
  In the machine
    Up to 2010: preijnection at 500 A, reset at 350 A
    Since 2011: no preinjection, 100 A reset to allow access

## Slide 5: 2010 precycle at 100 A
  600 s flattop
  Preinjection plateau 10 minutes at 500 A
  350 A reset
Precycle of the main dipoles 24 April 2011

## Slide 6: 2010 PHYSICS RUN AS PRECYCLE
  Main features
    Reset at 350 A
    Preinjection plateau at 500 A for 15 minutes
Typical physics run used as precycle – 25th April 2011

## Slide 7: 2011 precycle at 100 A
  600 s flattop
  Change: No preinjection plateau
  Change: 100 A reset
Precycle of the main dipoles 24 April 2011

## Slide 8: 2011 PHYSICS RUN AS PRECYCLE
  Main differences w.r.t. 2011 precycle
    Time at flattop (several hours): is 600 s enough to have reproducibility?
    Time at 100 A: around 1000 s, with some variability – is it relevant?
Typical physics run used as precycle – 25th April 2011

## Slide 9: CONCLUSIONS
  The precycle strategy has been optimized in 2011 to minimize turn around time
    Reproducibility is ensured – good match between pre-cycle and machine cycle
  We are operating the dipoles in pretty different conditions w.r.t. measurements
    No preinjection plateau
    Reset at 100 A
  The dependence on the history done in the past should be repeated in the new conditions – FiDeL coefficients estimated by N. Sammut et al cannot be used
    Campaign of measurements is needed
  Reproducibility could be further improved