## Slide 1: Intensity ramp-up
So far 3 fills with 768 bunches for a total of 8 hours
Need to have a couple of good fills (~12 hours each)
Next step to 912 bunches requires 108 bunches per injection (tried once during scrubbing)
The following 3 steps (1056/1200/1380) require 144 bunches/injection
To be done:
  Machine recovery after technical stop
  ALICE polarity reversal (TDI alignment + TCT set-up)
  Van der Meer scan
  TOTEM/ALPHA beam based alignment
  Set-up of the damper with optimized gain for higher frequencies (before Saturday. Wolfgang away for 1 week then). Feasible?
This is going to take the week end at least

## Slide 2: Intensity ramp-up (week 20)
Monday:
  Set-up of TCDI in TI2 for clean injection of 72 bunches (1 shift)
  Physics with 768 bunches
Tuesday:
  Set-up injection of 108 and 144 bunches
  After the set-up of injection inject up to 1200 and then up to 1380 bunches (trains of 144 bunches) and monitor RF, heat loads, vacuum (2-3 shifts). Experimental magnets will be ON. Anti-ecloud solenoids ON around MKI2 and MKI8.
Wednesday
  Physics with 768 bunches
Thursday
  Physics with 912 bunches with trains of 108 bunches (if OK from rMPP)
Friday
  Physics with 912 bunches

## Slide 3: Intensity ramp-up (week 21 and following)
Week-end
  Physics with 912 bunches
Beginning of week 21
  Might need 1 shift for setting up of the damper for high frequency (1 shift if not possible at start-up after technical stop)
  Physics with 1056 bunches if OK from rMPP (144 bunches per train)
Starting from week 21: ramp-up according to criteria defined by rMPP:
  144 bunches steps after 5 fills and 30 hours of stable beams (3 steps: 1056-1200 and 1380)

## Slide 4: Questions
After the observation of the beam losses during frequency trim we came to the conclusion that frequency ramp and acceleration rate are two fast. We should limit them to lower values? To which values?
Requirements in terms of monitoring from RF?